## Slide 1
LIBERO-SMART
Instruction following over familiar manipulation skills
Held-out instructions, skill combinations, object-target relations and layouts
3
suites
120
tasks
6,000
evaluation instances
Semantic
Fine-grained semantic following
40 tasks 2,000 instances
Only approach
the bowl.
Stop before grasping.
Paraphrases / subtasks / atomic actions
Logical constraints
Object / space / order / stop / hold
Visual Prompt (Vis)
Multimodal instruction understanding
40 tasks 2,000 instances
Place the bowl
inside the red circle.
Bind the cue to
the current target.
Visual target selection + localization
Circle
Region
Point
Path
Control
Mid-execution corrective control
40 tasks 2,000 instances
No, place it in
the ramekin instead.
Redirect the
remaining actions.
Goal correction
Process replanning
Matched intermediate states
Initialization coverage
10 macro layouts × 5 local variants
Layout 1
Layout 2
… Layout 10
50 initializations / task
Control: the same intermediate start per instance
Trajectory-level task contract
Correct target G
Objects and relations
Valid process H
Restrictions and order
Stable result R
Release / hold / stability
Direct: reach strict success within budget and maintain it for 30 more steps
Agentic: strict contract at termination
Goal-only is auxiliary. Strict success includes process and stability.
Benchmark results
† Agentic systems
LIBERO-SMART average strict success (%)
π0.5
7.18
SmartVLA-Pi
14.67
SmartVLA-OFT
14.03
Evaluation trajectories are excluded from adaptation. Tasks, initializations and budgets are matched within each protocol.
25
50
75
100%
LIBERO
PLUS
PRO
SMART
RT-FULL
RT-C2R
SmartVLA-Pi
SmartVLA-OFT
OpenVLA
OpenVLA-OFT
π
0
π
0.5
X-VLA
StarVLA
GR00T N1.6
ABot-M0
FineVLA
APT
CaP-X†
π
0.5
†
Agentic+SmartVLA-Pi†
Notes: Sources: sections/libero_smart.tex; tables/table_smart_suite_composition.tex; sections/appendix_benchmark_protocol.tex (app:smart-init, app:smart-contract, app:smart-aggregation, app:smart-training-boundary); sections/introduction.tex; source output/ppt/libero-smart.pptx. Core concept: familiar manipulation skills are evaluated under held-out instructions, skill combinations, object-target relations and layouts. Counts: 3 suites × 40 tasks × (10 macro layouts × 5 local variants) = 6,000 instances. For each Control instance, models start from the same intermediate physical state within the evaluation protocol. G/H/R apply jointly: current goal correctness, history-dependent restrictions/order and a semantically valid stable outcome. Direct policies attain strict success within the original budget and maintain it for all 30 subsequent action steps; the window may extend only to finish this holding check. Agentic systems satisfy the contract at termination with task-specific stability/release/holding requirements and history checks, without an extra 30-step window. Goal-only is auxiliary. Evaluation trajectories are excluded from adaptation, not asserted to be absent from every foundation model pretraining set. Three source scene images and the representative commands illustrate documented requirements rather than introducing new model rollout evidence. Original benchmark radar, all its model labels and curves, and the original strict-success values 7.18/14.67/14.03 are retained as auxiliary results. The source radar remains editable native vectors and labels. New schematic layout variants and cues are native editable diagram objects. Icons: Lucide 1.8.0, ISC, https://lucide.dev.